## Slide 1: Packet switching
Packet switching is a method or technique in which data is transferred in the form of manageable small chunks called packets.
It also means that a single block can tie up a router-router line for minutes, rendering message switching useless for interactive traffic.
It has the ability to send data packets over any path rather than fixed as in circuit switching because when data s divided into packets then those packets find their own path.

## Slide 2: Packet switching operation
Data are transmitted in short packets. Typically an upper bound on packet size is 1000 octets.
If a station has a longer message to send ,it breks up into a series of small packets.
The control information should at least contain:
Destination
Source address
Store and forward: Packets are received,stored briefly and pass onto the next node.

## Slide 3: Advantages of Packet switching
Line efficiency
Single node to link can be shared by many packets over time
Packets queued and transmitted as fast as possible
Data rate conversion
Each station connects to the local node at its own speed
Nodes buffer data if required to equalize rates
Packets are accepted even when networks is busy
Delivery may slow down
Priorities can be used