## Slide 1: Unit 12 Other Technological Reviews

## Slide 2: Contents
PSTN
ISDN and its types
Frame Relay
DSL and ADSL
VoIP
Bluetooth
Wi-Fi and Wi-Max
GSM
3G and 4G
NFC

## Slide 3: PSTN
Public Switched Telephone Network also known as “Plain Old Telephone Service”
A circuit switched network, i.e. phone call is switched through numerous switches like local ,regional , national, etc.
Circuit
    Connection ultimately established by among phones through switching
Prior to 1960s, phone calls were analog and manual , hence required operator’s assistance

## Slide 4: PSTN
Dialing techniques
  Pulse dialing / Rotary Dialing
  Touch Tone Dialing
Bandwidth link of PSTN
  64 Kbps
Dial-up Modem utilizes upto 56 kbps for data

## Slide 5: ISDN
Integrated Services Digital Network
Set of standards for digital transmission over telephone copper wire and other media.
Requires ISDN adapters at both ends
Broadband ISDN is intended for fiber optics supporting bandwidth up to 622.08Mbps
Two types of Channels of ISDN
  B (bearer) channel
    64kbps channel used for general purpose
  D (delta) channel
    16 or 64kbps channel for signaling between ISDN network and ISDN equipment

## Slide 6: ISDN
Types / Levels of ISDN service:
  Basic Rate Interface (BRI)
    Used for home users and small enterprises
    Also known as “2B+D” channel
    2B means 2 different B channels each of 64 kbps and D means one D channel of 16kbps
    Total data rate of BRI is hence 144Kbps
  Primary Rate Interface (PRI)
    Intended for large organizations with intensive communication needs
    Also known as 23B+D channel
    23 64kbps B channel and one 64 kbps D channel exists
    Standard for Europe : 30B+D and North America: 23B+D

## Slide 7: Frame Relay
High performance and simplified WAN protocol based on the principle of packet switching
Routes frames of data to different destinations based on the header information
Switches and routes data frames much faster but does not guarantee data integrity at all
Cares about speed, not the integrity
Operates at data link layer and physical layer

## Slide 8: Frame Relay
Frame relay provides connection oriented data link layer communication, by using virtual circuit
Two types of Virtual Circuit are used
  Switched VCs (SVCs)
    VC is established only when data needs to be transmitted and closed when transfer completed
    Temporary in nature
  Permanent VCs (PVCs)
    Permanently established virtual circuits whether or not the transmission is currently active or not
    Useful for frequent and consistent data transfer

## Slide 9: DSL
Digital Subscriber Line
Assumes that digital data requires no conversion into analog
Technology that brings high bandwidth information to homes and small business over copper telephone lines
DSL line can carry both data and voice signals at the same time

## Slide 10: DSL
Upstream and downstream lines exist
Protocols used
  DHCP (for IP address details provision to equipments)
  PPP(Point-to-point protocol)
    For user authentication
  PPPOE(Point to Point Protocol Over Ethernet) and PPPOA(Point to Point Protocol Over ATM)
    To provide Network Details

## Slide 11: Variations of DSL
ADSL
  Assymetric Digital Subscriber Line
HDSL
  High bit-rate DSL
RADSL
  Rate Adaptive DSL
VDSL
  Very high data rate DSL

## Slide 12: ADSL
Asymetric variety of DSL in which most of the bandwidth is devoted towards downstream
Small portion of data bandwidth allocated for upstream and user interaction
Downstream upto 6.1Mbps while upstream upto 640Kbps

## Slide 13: ADSL Operation
Frequency of 1100kHz, i.e. 1.1 MHz is divided into 256 channels each channel being of 4312.5 Hz , typically 4kHz
Uses a frequency splitter device to perform the above operation
Channels
  Channel 0 : 0-4312Hz used for PSTN
  Channel 1-5 : 4312Hz to 25875 Hz for guard band
  25kHz – 138 kHz for upstream
  138-1100kHz for Downstream

## Slide 14: ADSL frequency partition

## Slide 15: VOIP
Voice Over Internet Protocol
Allowing to make phone calls over an internet connection, instead of conventional telephone technologies like GSM, CDMA , PSTN, etc
Call is made through the internet and the voice is packetized
Audio of the voice is sampled and converted to digital format using the VOIP codec
Communication needs to happen in real time and for that, RTP (real time protocol ) is used

## Slide 16: VOIP
UDP is used in VOIP because it requires faster transmission more than quality transmission and retransmission
VOIP signaling protocols must be compatible with the traditional telephone signaling protocol , i.e. SS7
Components required for IP telephone system
  IP telephone
  Media gateway controller
  Media gateway (audio translation : IP and PSTN)
  Signaling gateway (signaling operations : IP and PSTN)

## Slide 17: Bluetooth
Short range radio technology used for Personal Area Network
Aims to replace wired communication for short distances
Transmission of signals over short distances 1m-100m typically. Radius based coverage area and varies from Class of service
  Class 1, 2 and 3: 100m, 10m and 1m respectively
Mainly for data and voice communication
Operates on unlicensed band of 2.4 – 2.485Ghz frequency
Data rate in Version 2.0 : 2.1-3Mbps
  V3 and V4 : 25Mbps
  V5 : 50Mbps
Topologies used
  Piconet
  Scatternet

## Slide 18: GSM
Global System for Mobile communication
Globally accepted standard for digital cellular communication
Operates at radio frequency 900MHz and is a narrowband based technology
Three major systems comprise of GSM
  Switching System
  Base Station System
  Operation and Support System

## Slide 19: a. Switching system
Responsible for call processing and subscriber related functions
Functional units of switching system
  Home location register
    Maintains profile of subscribers in a database
  Mobile service switching centre
    Performs telephone switching and controlling of calls
  Visitor Location register
    Contains temporary information about subscribers required by MSC to service the visiting subscriber

## Slide 20: a. Switching system
Functional units of switching system
  Authentication Centre (AUC)
    Authentication and encryption parameters that verify user’s identity and confidentiality of each call
    Detecting valid users and protecting the calls in progress
  Equipment Identity Register (EIR)
    Database used to identify valid and invalid mobile equipment
    Helps to prevent calls from stolen and unauthorized equipments

## Slide 21: b. Base Station System
Station related and radio related tasks are handled
Components
  Base Station Controllers
    Control functions like handover, cell configuration data, controlling radio frequency power, etc
  Base Transceiver Stations
    Radio equipments and antennas needed to service each cell in the network. These are mounted on top of houses
    Collectively controlled by the BSCs

## Slide 22: c. Operation and Support System
Functional entity from which the network operator monitors and controls the system
Offers support for operations and maintenance activities required for a GSM network
Must be connected to all equipment in the switching system and BSC

## Slide 23: 3G
3G stands for third generation
1800 - 2100MHz frequency, hence shorter coverage than GSM (2G)
Ability to properly transfer voice and non voice data over the same network due to improved bandwidth
Deliver broadband capacity and more customers can be accomodated
Standards
  Wideband CDMA
  EVDO (evolution data optimized)
Data rate of 2Mbps
More secure encryption than 2G

## Slide 24: 4G
Fourth Generation
Successor of 3G
2 – 8GHZ frequency range
High speed data rates : 20Mbps – 100Mbps
  Suitable for multimedia related functions like video streaming, TV broadcast, Video Calls, Mobile gaming, etc
LTE
  Long Term Evolution
  100Mbps downlink and 50Mbps uplink