## Slide 1: Central Processing Unit (CPU)
CPU Organizations
Instruction Formats
Addressing Modes
RISC and CISC Characteristics

## Slide 2: Central Processing Unit (CPU)
CPU performs the bulk of data-processing operations
It consists of 3 major parts:
  Register set: stores intermediate data during execution of an instruction
  ALU: performs various micro-operations required
  Control unit: supervises register transfers and instructs ALU
On the basis of the general organization of CPU register, CPU architecture can be:
  RISC, and
  CISC
On the basis of memory usage for program and data, CPU architecture can be:
  Stored program concept (Von Neumann architecture) architecture
  Harvard Computer architectures

## Slide 3: Contd..
Major components of CPU is as shown in below fig:

## Slide 4: Questions
What is the function of CPU? Explain the parts of CPU in detail.
Differentiate between Harvard architecture and Von Neumann architecture.

## Slide 5: General register organization
The block diagram of register organization inside the CPU is shown in the next slide.
It describe how each register communicates with the ALU through buses.

## Slide 7: General Register Organization (contd..)
Control Word for above CPU is as below:
Encoding of the register selection fields and ALU operations is given below:

## Slide 8: Contd..

## Slide 9: Contd..
Example:
Binary control word for this micro-operation statement is:

## Slide 11: Stack Organization
This is useful last-in, first-out (LIFO) list (actually storage device) included in most CPU’s.
Stack in digital computers is essentially a memory unit with a stack pointer (SP).
SP is simply an address register that points stack top.
Two operations of a stack are the insertion (push) and deletion (pop) of items.
In a computer stack, nothing is pushed or popped; these operations are simulated by incrementing or decrementing the SP register.

## Slide 12
Register stack
  It is the collection of finite number of registers.
  Stack pointer (SP) points to the register that is currently at the top of stack.

## Slide 14
Memory stack
  A portion of memory can be used as a stack with a processor register as a SP.
  Figure below shows a portion of memory partitioned into 3 parts: program, data and stack.

## Slide 17: Processor Organization
In general, most processors are organized in one of 3 ways:

## Slide 19: Types of instruction
Instruction format of a computer instruction usually contains 3 fields: operation code field (opcode), address field and mode field.
The number of address fields in the instruction format depends on the internal organization of CPU.
On the basis of no. of address field we can categorize the instruction as below:
Three-Address Instructions
  Computers with three-address instruction formats can use each address field to specify either a processor register or a memory operand.

## Slide 20
Two-Address Instructions
  These instructions are most common in commercial computers.
  Program to evaluate X = (A + B) * (C + D):

## Slide 21
One-Address Instructions
  One-address instruction uses an implied accumulator (AC) register for all data manipulation.
  All operations are done between AC and memory operand.
  Program to evaluate X = (A + B) * (C + D):

## Slide 22
Zero-Address Instructions
  A stack-organized computer uses this type of instructions.
  Program to evaluate X = (A + B) * (C + D):

## Slide 24: Addressing Modes
Operation field of an instruction specifies the operation that must be executed on some data stored in computer register or memory words.
The way operands (data) are chosen during program execution depends on the addressing mode of the instruction.
So, addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually referenced.
We use variety of addressing modes to accommodate one or both of following provisions:
  To give programming versatility to the user (by providing facilities as: pointers to memory, counters for loop control, indexing of data and program relocation)
  To use the bits in the address field of the instruction efficiently

## Slide 25: Types of Addressing mode
Implied Mode
  Address of the operands is specified implicitly in the definition of the instruction.
    No need to specify address in the instruction
    Examples from Basic Computer CLA, CME, INP
  ADD X;
  PUSH Y;
Immediate Mode
  Instead of specifying the address of the operand, operand itself is specified in the instruction.
    No need to specify address in the instruction
    However, operand itself needs to be specified
    Sometimes, require more bits than the address
    Fast to acquire an operand

## Slide 26
Register Mode
  Address specified in the instruction is the address of a register
    Designated operand need to be in a register
    Shorter address than the memory address
    A k-bit address field can specify one of 2k registers.
    Faster to acquire an operand than the memory addressing
Register Indirect Mode
  Instruction specifies a register which contains the memory address of the operand.
    Saving instruction bits since register address is shorter than the memory address
    Slower to acquire an operand than both the register addressing or memory addressing
    EA(effective address) = content of R.

## Slide 27
Auto-increment or Auto-decrement Mode
  It is similar to register indirect mode except that the register is incremented or decremented after (or before) its value is used to access memory.
  When address stored in the register refers to a table of data in memory, it is necessary to increment or decrement the register after every access to the table.
Direct Addressing Mode
  Instruction specifies the memory address which can be used directly to access the memory
    Faster than the other memory addressing modes
    Too many bits are needed to specify the address for a large physical memory Space
    EA= IR(address)

## Slide 28
Indirect Addressing Mode
  The address field of an instruction specifies the address of a memory location that contains the address of the operand
  When the abbreviated address is used large physical memory can be addressed with a relatively small number of bits
  Slow to acquire an operand because of an additional memory access
  EA= M[IR (address)]
Relative Addressing Modes
  The Address field of an instruction specifies the part of the address which can be used along with a designated register (e.g. PC) to calculate the address of the operand.
  Address field of the instruction is short
  Large physical memory can be accessed with a small number of address bits

## Slide 29
3 different Relative Addressing Modes:
PC Relative Addressing Mode:
  EA = PC + IR(address)
Indexed Addressing Mode
  EA = IX + IR(address) { IX is index register }
Base Register Addressing Mode
  EA = BAR + IR(address)

## Slide 32: Data Transfer and manipulation
Data Transfer and Manipulation
  Computers give extensive set of instructions to give the user the flexibility to carryout various computational tasks.
  The actual operations in the instruction set are not very different from one computer to another although binary encodings and symbol name (operation) may vary.
  So, most computer instructions can be classified into 3 categories:
    1. Data transfer instructions
    2. Data manipulation instructions
    3. Program control instructions

## Slide 33: Data Transfer instructions
Data transfer instructions causes transfer of data from one location to another without modifying the binary information content.
The most common transfers are:
  between memory and processor registers
  between processor registers and I/O
  between processor register themselves
Table below lists 8 data transfer instructions used in many computers.

## Slide 35
Instructions described above are often associated with the variety of addressing modes.
Assembly language uses special character to designate the addressing mode. E.g. # sign placed before the operand to recognize the immediate mode. (Some other assembly languages modify the mnemonics symbol to denote various addressing modes, e.g. for load immediate: LDI).
Example: consider load to accumulator instruction when used with 8 different addressing modes:

## Slide 37: Data manipulation Instructions
Data manipulation instructions provide computational capabilities for the computer.
These are divided into 3 parts:
  Arithmetic instructions
  Logical and bit manipulation instructions
  Shift instructions

## Slide 38: Arithmetic instructions

## Slide 39: Logical and bit manipulation instructions

## Slide 40: Shift instructions
Shifts instruction may be:
  Logical shifts
  Arithmetic shifts
  Rotate-type operations

## Slide 41: Program control instructions
Instructions are always stored in successive memory locations and are executed accordingly.
But sometimes it is necessary to condition the data processing instructions which change the PC value accidently causing a break in the instruction execution and branching to different program segments.

## Slide 42: RISC and CISC
An important aspect of computer architecture is the design of the instruction set for the processor.
Early computers had small and simple instruction sets, forced mainly by the need to minimize the hardware used to implement them.
As digital hardware became cheaper with the advent of ICs, computer instructions tended to increase both in number and complexity.
Many computers have instruction sets that include 100-200 instructions employing variety of data types and large number of addressing modes and are classified as Complex Instruction Set Computer(CISC).
In early 1980s, a number of computer designers recommended that computers use fewer instructions with simple constructs so as to execute them faster with in CPU without using memory as often. This type of computer is classified as a Reduced Instruction Set Computer(RISC).

## Slide 43: CISC
One reason to provide a complex instruction set is the desire to simplify the compilation (done by compilers to convert high level constructs to machine instructions) and improve the overall computer performance.
Essential goal: Provide a single machine instruction for each statement in high level language.
Examples: Digital Equipment Corporation VAX computer and IBM 370 computer.
Characteristics:
  A large no of instructions - typically from 100 to 250 instructions.
  A large variety of addressing modes –typically form 5 to 20.
  Variable-length instruction formats
  Instructions that manipulate operands in memory

## Slide 44: RISC
Main Concept: Attempt to reduce execution time by simplifying the instruction set of the computer.
Characteristics:
  Relatively few instructions and addressing modes.
  Memory access limited to load and store instructions
  All operations done with in CPU registers (relatively large no of registers)
  Fixed-length, easily decoded instruction format
  Single cycle instruction execution
  Hardwired rather than Micro-programmed control
  Use of overlapped-register windows to speed procedure call and return
  Efficient instruction pipeline